## Slide 1: FPGA-Based SoC Platform for Prototyping and Evaluation
Jonathan Ekman, Brenden Moran
Advisor : Dr. Reza Khani

## Slide 2: About Us
Jonathan Ekman
Cupertino, CA
Electrical Engineering Major
Project Manager Spring Semester
Brenden Moran
Paradise, CA
Computer Engineering Major
Assistant to the Project Manager
Dr. Reza Khani
Assistant Professor
EECE Department, CSU Chico
Advisor
Students
Notes: Intro to who we are slide, same as before, nothing has changed

## Slide 3: Agenda
Background and Design Motivation
Project Goals and Metrics
Design Choices
Implementation
Final Design Overview
Testing and Verification
Conclusions and Future Improvements
Notes: Agenda, what we are going to cover in our 12 minutes of time

## Slide 4: Background
The Problem
  Traditional Performance gains have plateaued
    Moore’s Law
    Dennard Scaling
  Engineers are focusing more on specialized SoC and multi-core designs
    Need a platform that enables testing for these custom designs
Solution
  Build a configurable multi-core analysis platform
  Measures latency, bandwidth, and resources used
Notes: Background, at most 1 min. Very brief explanation about the motivation behind our design

## Slide 5: Project Goals
A highly configurable FPGA project SoC built for academia
  Multicore capabilities
  DDR Ram access
  I/O ports
  Custom Accelerators
Embedded code to utilize all components as example
Notes: What our project is and the types of measurments we can get from this design like what we should expect as our final product and how we can measure that
Maybe be multiple slides of:
We want our project to do this
This is how we are going to achieve this
These are the types of measurments we can do to confirm the workings of our design
This is why we need a proof of concept with our accelerator

## Slide 6: metrics
CPU performance
  Clock cycles for an algorithm
  Cache performance
System Performance
  Bandwidth, latency in data W/R
Design performance
  Max allowable clock, FPGA space usage
Notes: Go in depth about accelerator logic and the ideas behind it
Why we chose matrix multiplication (AI and whatnot)
The logic behind our accelerator
How it works, high-level no actual code here

## Slide 7: Design choices
FPGA Suite
  AMD or Intel tools and FPGAs
    AMD was chosen as the tools are superior
Accelerator
  Matrix multiplication was chosen due to its practical nature
  Systolic array method was used because it is superior
    Performs multiplication faster using parallel compute
  Direct memory access
    Chosen due to the inconvenience and resource usage of loading data
Vitis
  Chose number identification as a simple and interesting usage of accelerator
Notes: How we create our project, the kind of components that will give us the best option for our design
We already talked about the accelerator so now its what system do we want this to be apart of, talk aqbout the components we already chose from last semester but now include what makes them better for this design as well
Microblaze has no on chip multiplier circuit
Very basic fpga board design

## Slide 8: MULTICORE
The connection of 2+ cores
  Cores must communicate
Issues
  Lack of Cache Coherency
    Solved by manually managing cache
    Cache coherency is available for more advanced FPGAs
  Core identification and Reset vector
    Each core has unique machine thread id (MhartId)
    Each core has unique reset vector
      Without unique vector special measures must be taken
Tested with two core matrix multiplication Result in minicom -->
  Test was successful

## Slide 9: Accelerator
Multicore Design Worked Well However :
  MicroBlaze V is free to use but logic is not open source 
    Need access to its internal pipeline stages
  Takes up a large number of resources 
  Has multiple use cases 
Accelerator
  Customizable to our design 
  Specialized for our specific use case (matrix multiplication) 
  Takes up much smaller number of resources 
  Has only one use case 
  Can use direct memory access 
  Much faster 

## Slide 10: Block Diagram: Simplified
MicroBlaze V
  Main processor running the code
Smart Connect
  Communication to all components through AXI
DMAs
  Stream input/output matrices to our accelerator.
DDR 2
  Main memory, storing all data.
Notes: Our block diagram – simple, what our simple diagram looks like for testing and measurements

## Slide 11: Detailed Block Diagram
Notes: Maybe detailed block diagram, this should be a what we started with and what we have now kind of thing
Go into the connections of each thing independently for more detail on how the communicate
Talk about the axi bus
Mention the smart connect being the home for all components to communicate with preset addresses
Speak on the matrix multiplication module and how we had to create it as a custom IP with AXI lite and stream connections

## Slide 12: Testing
What metrics do we want to test?
  Latency (see if accelerator improves latency)
  Bandwidth
  Area used on chip/resources used
  BONUS
    Cache misses/hits
What kind of test we want
  Algorithm that uses matrix multiplication heavily to compare using the accelerator with not using it
  Alter this algorithm to use the APM to measure bandwidth of the accelerator's output
Vivado Design Suite does this for us!
Notes: Testing
What values do we want to test to see
How are we going to test it (what algorithm we are going to use and how our accelerator works with it)
Brief overview of algorithm like a flowchart or something, This is not the main thing we want to show, this code was taken from online just modified to work with our custom hardware so make that apparent
What the outputs are and what each of them mean

## Slide 13: Testing Algorithm
Sudo number identification using matrix multiplication
  Similar to how neural networks identify images based on weighted entries
  Takes in an input matrix representing a number
  Multiplies it across 10 preset matrices being numbers 0-9
  Sums the diagonals (trace) of each output matrix to find best match
This is matrix multiplication heavy (10 total runs)
Many similar algorithms can be found online

## Slide 14: Results
Latency
  Using accelerator: 41 ms
  Not using accelerator: 122 ms
  ~3x improvement
Bandwidth
  61 kB/s
Resources Used
  35,000 Slice LUTs (lookup tables)
    1/2 of total LUTs on board
  30,000 Slice Registers
    1/4 of total registers on board
  13.5 Block RAM Tile
    1/10 of total block RAM on board
Max Frequency
  117MHz fast for FPGA softcore
Notes: Conclusions gathered from the test and metrics gained.
Where this can be used in the future (others can take our design and make it better (pipeline it, make it parallel, instantiate more to run all in parallel) or they can test their own (import their own custom IP to test metrics))

## Slide 15: Conclusions
Goal
Configurable multi-core analysis platform.
  Customizable with unique SoC
  Measurable metrics
    Latency
    Bandwidth
    Resources Used
What We Achieved
FPGA-based prototyping platform used for analysis
  Custom SoC accelerator
  Open-source GitHub for others to use our design and make their own
  Measurable metrics
    Latency
    Bandwidth
    Resources Used
Future Improvements:
Add more accelerators
  Improve parallelism
Pipeline the accelerator
Improve accelerator logic

## Slide 16: References
[1] “Moore’s law: The number of transistors per microprocessor,” Our World in Data. [Online]. Available: https://ourworldindata.org/grapher/transistors-per-microprocessor. [Accessed: Sep. 30, 2025].
[2] V. Sekar, “How Dennard scaling allowed transistors to shrink,” Vik’s Newsletter, Jan. 12, 2025. [Online]. Available: https://www.viksnewsletter.com/p/how-dennard-scaling-actually-works. [Accessed: Sep. 30, 2025].
[3] AMD, MicroBlaze V Processor Reference Guide, UG1629. [Online]. Available: https://docs.amd.com/r/en-US/ug1629-microblaze-v-user-guide/Introduction. [Accessed: Nov. 30, 2025].
[4] AMD, “MicroBlaze V RISC-V processor overview,” Aug. 7, 2025. [Online]. Available: https://www.amd.com/en/products/software/adaptive-socs-and-fpgas/microblaze-v.html. [Accessed: Nov. 30, 2025].
[5] Arm Ltd., “Multi-core processors,” Arm Developer Documentation, 2025. [Online]. Available: https://developer.arm.com/documentation/den0013/0400/Multi-core-processors. [Accessed: Nov. 30, 2025].
[6] RISC-V International, “Ratified RISC-V specifications.” [Online]. Available: https://riscv.org/specifications/ratified/. [Accessed: Nov. 30, 2025].
[7] D. S. Roy, “Systolic matrix multiplier,” Digital System Design, Jun. 12, 2020. [Online]. Available: https://digitalsystemdesign.in/systolic-matrix-multiplier/. [Accessed: Dec. 18, 2025].
[8] IEEE Standards Association, IEEE Standard for SystemVerilog—Unified Hardware Design, Specification, and Verification Language, IEEE Std 1800-2017. Piscataway, NJ, USA: IEEE, 2017.
[9] National Institute of Standards and Technology (NIST), Framework for Improving Critical Infrastructure Cybersecurity, Version 1.1. Gaithersburg, MD, USA: NIST, 2018.
[10] N. Dave, K. Fleming, M. King, M. Pellauer, and M. Vijayaraghavan, “Hardware acceleration of matrix multiplication on a Xilinx FPGA,” in Proc. IEEE Int. Workshop on Memory System Performance and Correctness (MEMPOD), May 2007, pp. 97–100, doi: 10.1109/MEMCOD.2007.371239.
[11] A. Peiris, “Digital design of systolic array architecture for matrix multiplication,” Ashan’s Blog, Aug. 1, 2015. [Online]. Available: https://ashanpeiris.blogspot.com/2015/08/digital-design-of-systolic-array.html. [Accessed: Dec. 18, 2025].
Notes: References

## Slide 17: Thank You!
Any Questions?

## Slide 18: Systolic Array Accelerator
1*2
+ 2*4
+ 3*6
1*1
+ 2*5
+ 3*9
4*2
+ 5*4
+ 6*6
Notes: Backup slides in case we get questions about it